Some numbers and their ‘meaning’
- These numbers occur very frequently in discussion
- 0x 80000000 = 2 GB = KERNBASE
- 0x 100000 = 1 MB = EXTMEM
- 0x 80100000 = 2GB + 1MB = KERNLINK
- 0x E000000 = 224 MB = PHYSTOP
- 0x FE000000 = 3.96 GB = 4064 MB = DEVSPACE
  - 4096 – 4064 = 32 MB left on top

---
X86 Memory Management

---
X86 address : protected mode address translation

---
X86 segmentation

---
X86 paging

---
Segmentation + Paging

---
Segmentation + Paging
Selector value is implicit based on address being accessed.
Instruction: CS
Stack Variable: SS
Data: DS
etc.

---
GDT Entry

---
Page Directory Entry (PDE)
Page Table Entry (PTE)

---
Segment selector
EFLAGS register

---
CR0
PG: Paging enabled or not WP: Write protecion on/off
PE: Protection Enabled --> protected mode.
CR2

---
CR3
CR4

---
Layout of process’s VA space

---
Memory Layout of a user process
After exec()
Note the argc, argv on stack
The “guard page” is just a mapping in page table. No frame allocated. It’s marked as invalid. So if stack grows (due to many function calls), then OS will detect it with an exception

---
Memory Layout of a user process
On sbrk()
The system call to grow process’s address space. Calls growproc()
growproc()
Allocate a frame, Add an entry in page table at the top (above proc->sz)
//This entry can’t go beyond KERNBASE
Calls switchuvm()
Switchuvm()
Ultimately loads CR3, invalidating cache

---
mmu.h : paging related macros
#define PTXSHIFT 12 // offset of PTX in a linear address
#define PDXSHIFT 22 // offset of PDX in a linear address
#define PDX(va) (((uint)(va) >> PDXSHIFT) & 0x3FF)// page directory index
#define PTX(va) (((uint)(va) >> PTXSHIFT) & 0x3FF)// page table index
// construct virtual address from indexes and offset
#define PGADDR(d, t, o) ((uint)((d) << PDXSHIFT | (t) << PTXSHIFT | (o)))
// +--------10------+-------10-------+---------12----------+
// | Page Directory | Page Table | Offset within Page |
// | Index | Index | |
// +----------------+----------------+---------------------+
// \--- PDX(va) --/ \--- PTX(va) --/

---
mmu.h : paging related macros
// Page directory and page table constants.
#define NPDENTRIES 1024 // # directory entries per page directory
#define NPTENTRIES 1024 // # PTEs per page table
#define PGSIZE 4096 // bytes mapped by a page
#define PGROUNDUP(sz) (((sz)+PGSIZE-1) & ~(PGSIZE-1))
#define PGROUNDDOWN(a) (((a)) & ~(PGSIZE-1))

---
mmu.h : paging related macros
// Page table/directory entry flags.
#define PTE_P 0x001 // Present
#define PTE_W 0x002 // Writeable
#define PTE_U 0x004 // User
#define PTE_PS 0x080 // Page Size
// Address in page table or page directory entry
#define PTE_ADDR(pte) ((uint)(pte) & ~0xFFF) // get all but last 12 bits
#define PTE_FLAGS(pte) ((uint)(pte) & 0xFFF) // get last 12 bits

---
mmu.h : Segmentation related macros
// various segment selectors.
#define SEG_KCODE 1 // kernel code
#define SEG_KDATA 2 // kernel data+stack
#define SEG_UCODE 3 // user code
#define SEG_UDATA 4 // user data+stack
#define SEG_TSS 5 // this process's task state

---
mmu.h : Segmentation related macros
// various segment selectors.
#define SEG_KCODE 1 // kernel code
#define SEG_KDATA 2 // kernel data+stack
#define SEG_UCODE 3 // user code
#define SEG_UDATA 4 // user data+stack
#define SEG_TSS 5 // this process's task state
#define NSEGS 6

---
mmu.h : Segmentation related macros
struct segdesc { // 64 bit in size
  uint lim_15_0 : 16; // Low bits of segment limit
  uint base_15_0 : 16; // Low bits of segment base address
  uint base_23_16 : 8; // Middle bits of segment base address
  uint type : 4; // Segment type (see STS_ constants)
  uint s : 1; // 0 = system, 1 = application
  uint dpl : 2; // Descriptor Privilege Level
  uint p : 1; // Present
  uint lim_19_16 : 4; // High bits of segment limit
  uint avl : 1; // Unused (available for software use)
  uint rsv1 : 1; // Reserved
  uint db : 1; // 0 = 16-bit segment, 1 = 32-bit segment
  uint g : 1; // Granularity: limit scaled by 4K when set
  uint base_31_24 : 8; // High bits of segment base address
};

---
mmu.h : Segmentation related code
// Application segment type bits
#define STA_X 0x8 // Executable segment
#define STA_W 0x2 // Writeable (non-executable segments)
#define STA_R 0x2 // Readable (executable segments)
// System segment type bits
#define STS_T32A 0x9 // Available 32-bit TSS
#define STS_IG32 0xE // 32-bit Interrupt Gate
#define STS_TG32 0xF // 32-bit Trap Gate

---
Code from bootasm.S bootmain.c is over!
Kernel is loaded.
Now kernel is going to prepare itself

---
main() in main.c
- Initializes “free list” of page frames
  - In 2 steps. Why?
- Sets up page table for kernel
- Detects configuration of all processors
- Starts all processors
  - Just like the first processor
- Creates the first process!
- Initializes
  - LAPIC on each processor, IOAPIC
  - Disables PIC
  - “Console” hardware (the standard I/O)
  - Serial Port
  - Interrupt Descriptor Table
  - Buffer Cache
  - Files Table
  - Hard Disk (IDE)

---
main() in main.c
int
main(void) {
  kinit1(end, P2V(4*1024*1024)); // phys page allocator
  kvmalloc(); // kernel page table
void
kinit1(void *vstart, void *vend) {
  initlock(&kmem.lock, "kmem");
  kmem.use_lock = 0;
  freerange(vstart, vend);
}

---
main() in main.c
kfree(char *v) {
  struct run *r;
  if((uint)v % PGSIZE || v < end || V2P(v) >= PHYSTOP)
    panic("kfree");
  // Fill with junk to catch dangling refs.
  memset(v, 1, PGSIZE);
  if(kmem.use_lock)
    acquire(&kmem.lock);
  r = (struct run*)v;
  r->next = kmem.freelist;
  kmem.freelist = r;
  if(kmem.use_lock)
    release(&kmem.lock); }
void
freerange(void *vstart, void *vend)
{
  char *p;
  p = (char*)PGROUNDUP((uint)vstart);
  for(; p + PGSIZE <= (char*)vend; p += PGSIZE)
    kfree(p);
}

---
Free List in XV6 Obtained after main() -> kinit1()
Pages obtained Between
end = 801154a8 = 2049 MB to P2V(4MB) = 2052 MB
Remember
Right now Logical = Physical address.
Actually like
this in memory
lock
kmem
uselock
Seen independently
run *freelist
run *
run *
run *

---
Back to main()
// Allocate one page table for the machine for the kernel address
// space for scheduler processes.
void
kvmalloc(void)
{
  kpgdir = setupkvm();
  switchkvm();
}
int
main(void) {
  kinit1(end, P2V(4*1024*1024)); // phys page allocator
  kvmalloc(); // kernel page table

---
Back to main()
// Allocate one page table for the machine for the kernel address
// space for scheduler processes.
void
kvmalloc(void)
{
  kpgdir = setupkvm(); // global var kpgdir
  switchkvm();
}
int
main(void) {
  kinit1(end, P2V(4*1024*1024)); // phys page allocator
  kvmalloc(); // kernel page table

---
pde_t*
setupkvm(void)
{
  pde_t *pgdir;
  struct kmap *k;
  if((pgdir = (pde_t*)kalloc()) == 0)
    return 0;
  memset(pgdir, 0, PGSIZE);
  if (P2V(PHYSTOP) > (void*)DEVSPACE)
    panic("PHYSTOP too high");
 for(k = kmap; k < &kmap[NELEM(kmap)]; k++)
    if(mappages(pgdir, k->virt, k->phys_end - k->phys_start,
        (uint)k->phys_start, k->perm) < 0) {
      freevm(pgdir);
      return 0;
    }
  return pgdir;
}

---
static struct kmap {
  void *virt;
  uint phys_start;
  uint phys_end;
  int perm;
} kmap[] = {
 { (void*)KERNBASE, 0, EXTMEM, PTE_W}, // I/O space
 { (void*)KERNLINK, V2P(KERNLINK), V2P(data), 0}, // kern text+rodata
 { (void*)data, V2P(data), PHYSTOP, PTE_W}, // kern data+memory
 { (void*)DEVSPACE, DEVSPACE, 0, PTE_W}, // more devices
};

---
kmap[] mappings done in kvmalloc(). This shows segmentwise, entries are done in page directory and page table for corresponding VA-> PA mappings
4B
DEVSPACE=3.96GB
KERNBASE+PHYSTOP=2.224GB= 2272MB
data= 2049.3125 MB
KERNBASE+EXTMEM=2049 MB
KERNBASE=2048MB
0
4GB
DEVSPACE=3.96GB
PHYSTOP = 224MB
1.03125 MB = 1MB + data
EXTMEM=1MB
0
Un
mapped
Unused
Kernel
data
+ memory
Kernel
data
+ memory
Kernel
code +
RO Data
I/O Space
Kernel
code +
RO Data
Process
 address
 space
I/O Space
0x80108000 =data = 2049.3125 MB
Is obtained from kernel.sym
Physical Memory
Logical Address space

---
Remidner: PDE and PTE entries

---
Before mappages()
pgdir

---
4K
Page-no,UWP
Page-no,UWP
Page-no,UWP
Page-no,UWP
Page-no,UWP
Page-no,UWP
Page-no,UWP
Page-no,UWP
Page-no,UWP
pgdir
4K
What mappages()
Does

---
RAM
After kvmalloc() in main()
Physical Addr
Linear Address
Logical Address = offset
Dir
pg
Offset
4MB
0
CS, SS, etc.
Base	Limit	Permissions
0	4GB	Write
0	4GB	Read, Execute
0	0	0
Selector
3
2
1
0
DS
SS
Page Table
GDT
CR3
CS
Now Linear Address = Logical Address != Physical Address
kpgdir

---
main()->seginit()
- Re-initialize GDT
- Once and forever now
- Just set 4 entries
  - All spanning 4 GB
  - Differing only in permissions and privilege level

---
RAM
After seginit() in main().
On the processor where we started booting
Physical Addr
Linear Address
Logical Address = offset
Dir
pg
Offset
4MB
0
CS, SS, etc.
Base	Limit	Permissions	DPL
0	4GB	Write	3
0	4GB	Read, Execute	3
0	4GB	Write	0
0	4GB	Read, Execute	0
0	0	0
Selector
4
3
2
1
0
DS
SS
Page Table
GDT
CR3
CS
Now Linear Address = Logical Address != Physical Address
kpgdir

---
After seginit()
- While running kernel code, necessary to switch CS, DS, SS to index 1,2,2 in GDT
- While running user code, necessary to switch CS, DS, SS to index 3,4,4 in GDT
- This happens automatically as part of “trap” handling (covered separately)

---
Memory Management

---
X86 page table hardware

---
Layout of process’s VA space

---
Memory Layout of a user process
After exec()
Note the argc, argv on stack

---
Memory Layout of a user process
The “guard page” is just a mapping in page table. No frame allocated. It’s marked as invalid. So if stack grows (due to many function calls), then OS will detect it with an exception

---
Memory Layout of a user process
On sbrk()
The system call to grow process’s address space. Calls growproc()
growproc()
Allocate a frame, Add an entry in page table at the top (above proc->sz)
//This entry can’t go beyond KERNBASE
Calls switchuvm()
Switchuvm()
Ultimately loads CR3, invalidating cache

---
Free List in XV6
Actually like
this in memory
lock
kmem
uselock
Seen independently
run *freelist
run *
run *
run *

---
exec()
- sys_exec()
  exec(path, argv)
- exec(parth, argv)
  ip = namei(path))
  readi(ip, (char*)&elf, 0, sizeof(elf)) != sizeof(elf)
  for(i=0, off=elf.phoff; i<elf.phnum; i++, off+=sizeof(ph)){
  if(readi(ip, (char*)&ph, off, sizeof(ph)) != sizeof(ph))
  if((sz = allocuvm(pgdir, sz, ph.vaddr + ph.memsz)) == 0)
  if(loaduvm(pgdir, (char*)ph.vaddr, ip, ph.off, ph.filesz) < 0)
  }

---
exec()
- exec(parth, argv)
  // Allocate two pages at the next page boundary.
  // Make the first inaccessible. Use the second as the user stack.
  sz = PGROUNDUP(sz);
  if((sz = allocuvm(pgdir, sz, sz + 2*PGSIZE)) == 0)
  // Push argument strings, prepare rest of stack in ustack.
  for(argc = 0; argv[argc]; argc++) {
  sp = (sp - (strlen(argv[argc]) + 1)) & ~3;
  if(copyout(pgdir, sp, argv[argc], strlen(argv[argc]) + 1) < 0)